## Slide 1: Design for Verification Project Update
2021-05-03
Eldrick Millares, Jack Humphries (eldrick, jhumphri@stanford.edu)

## Slide 2: Recap:
Completed Deployment on Steel (simple design)
Ongoing Deployment on BOOM (complex design)

## Slide 3: Steel Demo - Current Status
All instructions in current SQED generator supported (including load / store)
No counterexamples
  Except for when the qed_i_cache eventually gets full and can no longer buffer incoming original instructions

## Slide 4: Steel Demo - Summary of Notable Modifications
Disabled CSR MIE
Shrunk Main Memory
Accounted for when `SW` commits in the pipeline
Accounted for multiple commits in one cycle
Accounted for pipeline flushes
Summary of above is in README of the steelcore_demo/ in the Github repo

## Slide 5: Steel Demo - Next Steps
Enabling Control Flow Checking
  Can formulate some assertions on the Instruction Address values based on the CFCSS-V and CFTSS-V QED tests
  Further references to be found in David Lin’s dissertation
  Want to modify SQED Generator to allow these instructions
Adding “Location-Specific SIF Commit Tracking” for Improving BMC Depth
  Deals with cases where you have long pipelines where instructions commit at different points in the pipeline
  Commit = last modification of architectural state by instruction
  Requires special care in dealing with these scenarios, can decrease performance of technique if pipeline is long
  Dynamically track when SIF instructions commit and make that location (Reg File, Memory) individually QED consistent

## Slide 6: BOOM Demo - Current Status
Identified Signals of Interest
  Instruction Bus
  Register File Signals
  Renaming Table
Designing logic to account for register renaming when checking register file consistency

## Slide 7: Next Steps Summary
Extend ISA scope in SQED Generator / steel
Deploying QED module to generated BOOM verilog
Account for BOOM Register Renaming