## Slide 1
E-QED:
Electrical Bug Localization with
Quick Error Detection and Formal Methods
Eshan Singh, Clark Barrett, Subhasish Mitra
Stanford University
Notes: 1

## Slide 2
Source: Intel
2
Post-silicon bug count
Year
“Post-silicon cost & complexity rising faster than design cost” – S. Yerramilli, V.P., Intel
Design
Pre-silicon
Verification
Post-silicon
Validation
High Volume
Fab
Post-silicon Validation Critical
Notes: So the growing complexity of hardware design has led to an increasing number of bugs escape verification this is pre-silicon or done before the design is fabricated. As a result, these bugs can only be detected during post-silicon validation, when tests are run on the manufactured chip before it reaches high volume.

## Slide 3
Root-cause & fix
Run tests (e.g., OS, games)
Weeks or Months
Manual work per bug
Detect bugs
3
Localize bugs
Post-silicon Validation
Quick Error Detection
[Lin, IEEE TCAD 14]

## Slide 4
Focus on localization
Detect bugs
4
Localize bugs
Logic design bugs
  Symbolic QED [Singh, IEEE TCAD 17]
Electrical bugs
  E-QED: this paper
Bug Localization: BIG Problem
Notes: Big problem: localization

## Slide 5
5
Automatic, overnight
  vs. manual, weeks / months per bug
Fine-grained localization
  From 1 million to 20 flip-flops
Scalable: billion-transistor design
Small area impact: 2.5% or less
  Many ways to reduce area impact
E-QED

## Slide 6
6
Problem Setup
Electrical bug
Design RTL
Chip
0
0
1
0
1
0
0
1
1
0
1
1
0
1
0
1
1
0
0
1
1
1
1
1
Record
Test Inputs
Record
Test Outputs
Design
Inputs
Outputs
Electrical bug candidates (e.g., flip-flops)
…
…
1
1
0
1
0
0
1
1
CRASH!
// Memory Write Block
// Write Operation : When we_0 = 1, cs_0 = 1
always @ (address_0 or cs_0 or we_0 or data_0 47 or address_1 or cs_1 or we_1 or data_1)
begin : MEM_WRITE
if ( cs_0 && we_0 ) begin mem[address_0] <= data_0;
end else if (cs_1 && we_1) begin
mem[address_1] <= data_1;
end end
0
0
1
0
Find
inconsistencies
1
0
1
1
1
0
0
1
1
1
0
1
No electrical bug
Failure reproduction difficult
Full system simulation infeasible
Large designs: too big for formal tools
Challenges

## Slide 7
E-QED
Run post-silicon validation tests
Design phase: E-QED signature blocks
Localize error: formal methods
Notes: E-QED relies on several steps during three stages.
During the chip design phase, E-QED signature blocks are automatically inserted. These E-QED signature blocks are used during post-silicon validation to capture and compress the logic values of selected signals (signatures).
During post-silicon validation, a suite of tests is run—it is crucial to run tests with short error-detection latencies (QED tests). When an error is detected by such a test, the test is immediately halted, and all the captured signatures are scanned out.
In the last phase the collected signatures are analyzed with formal techniques to
First identify which Design Module produced the error(s)
Then to find the FFs in that Module that could have captured the error(s)
Finally to narrow this list even further by checking for consistency with signatures captured by neighboring Design Modules

## Slide 8
E-QED
Run post-silicon validation tests
Design phase: E-QED signature blocks
Localize error: formal methods
Notes: E-QED relies on several steps during three stages.
During the chip design phase, E-QED signature blocks are automatically inserted. These E-QED signature blocks are used during post-silicon validation to capture and compress the logic values of selected signals (signatures).
During post-silicon validation, a suite of tests is run—it is crucial to run tests with short error-detection latencies (QED tests). When an error is detected by such a test, the test is immediately halted, and all the captured signatures are scanned out.
In the last phase the collected signatures are analyzed with formal techniques to
First identify which Design Module produced the error(s)
Then to find the FFs in that Module that could have captured the error(s)
Finally to narrow this list even further by checking for consistency with signatures captured by neighboring Design Modules

## Slide 9
Design Phase
9
  Module size = fit formal tool
Too big for formal tools
Module A
Module D
Module
B
Module E
Module
C
Module F
Full
Design
Analyze modules separately
Notes: Restoration ratios, do not address bugs are gone by the time you look at it

## Slide 10
Insert Additional Hardware
10
E-QED signature blocks
Module A
Module D
Module
B
Module E
Module
C
Module F
Notes: Restoration ratios, do not address bugs are gone by the time you look at it

## Slide 11
Trace Buffer
11
Trace buffer
  All values captured
1 | 0 | 1
Trace buffer
MISR
0 | 1 | 1
1 | 0 | 0
0
0
0
0
0
1
1
0
1
0
0
0
0
1
1
0
1
1
1
0
1
0
1
0
Captured values
1
0
0
1
1
0
1
0
1
Multiple Input Signature Register
  Values compressed into signature
Area overhead
~L2 cache size
Area overhead
2.5%
1 | 1 | 0
0 | 0 | 1
1
1
0
0
1
0
0
1
1
1
0
1
0
1
0
0
0
1
Trace Buffer vs MISR
Notes: L2 cache -> largest component

## Slide 12
E-QED
Run post-silicon validation tests
Design phase: E-QED signature blocks
Localize error: formal methods
Notes: E-QED relies on several steps during three stages.
During the chip design phase, E-QED signature blocks are automatically inserted. These E-QED signature blocks are used during post-silicon validation to capture and compress the logic values of selected signals (signatures).
During post-silicon validation, a suite of tests is run—it is crucial to run tests with short error-detection latencies (QED tests). When an error is detected by such a test, the test is immediately halted, and all the captured signatures are scanned out.
In the last phase the collected signatures are analyzed with formal techniques to
First identify which Design Module produced the error(s)
Then to find the FFs in that Module that could have captured the error(s)
Finally to narrow this list even further by checking for consistency with signatures captured by neighboring Design Modules

## Slide 13
13
Quick Error Detection Critical
Capture bug activation for formal analysis
Short error detection latency a must
  < 1,000 cycles
Error
detected
Bug activated
Error occurred
Test
execution
Timeline
Error detection latency
Billions of cycles

## Slide 14
14
Quick Error Detection
Error
detected
Billions of cycles
Test
execution
Timeline
QED
[Lin, IEEE TCAD 14]
Error detected
< 1,000 cycles
Bug activated
Error occurred
Error detection latency
Error detection latency
Notes: No need to understand QED for E-QED

## Slide 15
E-QED
Run post-silicon validation tests
Design phase: E-QED signature blocks
Localize error: formal methods
Notes: E-QED relies on several steps during three stages.
During the chip design phase, E-QED signature blocks are automatically inserted. These E-QED signature blocks are used during post-silicon validation to capture and compress the logic values of selected signals (signatures).
During post-silicon validation, a suite of tests is run—it is crucial to run tests with short error-detection latencies (QED tests). When an error is detected by such a test, the test is immediately halted, and all the captured signatures are scanned out.
In the last phase the collected signatures are analyzed with formal techniques to
First identify which Design Module produced the error(s)
Then to find the FFs in that Module that could have captured the error(s)
Finally to narrow this list even further by checking for consistency with signatures captured by neighboring Design Modules

## Slide 16
Localization to a Design Module
16
Run QED post-silicon test
Error detected
Module A
Module D
Module
B
Module E
Module
C
Module F
Start analysis: Module A
Notes: Restoration ratios, do not address bugs are gone by the time you look at it

## Slide 17
17
Capture window = number of cycles compressed
MISR periodically reset
  Ensure capture window < 2,000 cycles
Capture window = 418 cycles
Localization to a Design Module
Module A
1 | 1 | 0 | 0 | 1 | 0
1 | 0 | 0 | 0 | 1 | 0
Input MISR
Output MISR
Notes: Restoration ratios, do not address bugs are gone by the time you look at it

## Slide 18
18
Bounded Model Checking: Module A
Module
RTL
Localization to a Design Module
BMC Tool
Module A
1 | 1 | 0 | 0 | 1 | 0
1 | 0 | 0 | 0 | 1 | 0
Input MISR
Output MISR
Constrain
final input signature
Constrain
final output signature
Unroll = 418 cycles
Capture window
Notes: Restoration ratios, do not address bugs are gone by the time you look at it

## Slide 19
19
Analyze Module A
Module
RTL
Localization to a Design Module
BMC Tool
Module A
1 | 1 | 0 | 0 | 1 | 0
1 | 0 | 0 | 0 | 1 | 0
Input MISR
Output MISR
Constrain
final input signature
Constrain
final output signature
Signatures
consistent

Notes: Restoration ratios, do not address bugs are gone by the time you look at it

## Slide 20
Localization to a Design Module
20
Next: Module E
Module A
Module D
Module
B
Module E
Module
C
Module F
Notes: Restoration ratios, do not address bugs are gone by the time you look at it

## Slide 21
21
Setup and analyze: Module E
Module
RTL
Localization to a Design Module
BMC Tool
Module
E
1 | 1 | 1 | 0 | 1 | 0
1 | 1 | 0 | 0 | 1 | 0
Input MISR
Output MISR
Constrain
final input signature
Constrain
final output signature
Unroll = 418 cycles
Capture window
Signatures inconsistent
Notes: Restoration ratios, do not address bugs are gone by the time you look at it

## Slide 22
22
Setup and analyze: Module E
Localization to a Design Module
BMC Tool
Module
E
1 | 1 | 1 | 0 | 1 | 0
1 | 1 | 0 | 0 | 1 | 0
Input MISR
Output MISR
Bug in Module E!
Notes: Restoration ratios, do not address bugs are gone by the time you look at it

## Slide 23
Localization to a Design Module
23
Module A
Module D
Module
B
Module E
Module
C
Module F





Notes: Restoration ratios, do not address bugs are gone by the time you look at it

## Slide 24
24
From 1 million to ~30,000 flip-flops
How can we do better?
Localization to a Design Module
Notes: Restoration ratios, do not address bugs are gone by the time you look at it

## Slide 25
Single Cycle Flip-Flop Error Model
25
Error source
  Exactly one flip-flop
    In exactly one clock cycle
  Prior studies
    [Mclaughlin, VTS 09;
    Killpack, IEEE D&T 08; Mak, IEEE D&T 04]

## Slide 26
Single Cycle Flip-Flop Error Localization
26
A
B
X
Y
Z
F1
F2
F3
F4
F5
F6
F7
F8
Module E
Input MISR
Output MISR
1 | 1 | 1 | 0 | 1 | 0
1 | 1 | 0 | 0 | 1 | 0
Module
E
Initial example: ignore MISRs
Notes: Restoration ratios, do not address bugs are gone by the time you look at it

## Slide 27
Single Cycle Flip-Flop Error Localization
27
A
B
X
Y
Z
F1
F2
F3
F4
F5
F6
F7
F8
1
1
1
1
1
1
1
0
1
1
0
1
1
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Fault-free sequence
Notes: Restoration ratios, do not address bugs are gone by the time you look at it

## Slide 28
28
A
B
X
Y
Z
F1
F2
F3
F4
F5
F6
F7
F8
0
1
1
1
1
1
Error!
Cycle 4
1
Candidate FFs
Cycle 4: F6
Potential candidate
Single Cycle Flip-Flop Error Localization
Error at X
Try F6
Notes: Restoration ratios, do not address bugs are gone by the time you look at it

## Slide 29
29
A
B
X
Y
Z
F1
F2
F3
F4
F5
F6
F8
1
1
1
1
1
1
Error!
Cycle 3
0
Cycle 4
F7
1
1
1
Candidate FFs
Cycle 4: F6
Potential candidate
Cycle 3: F3
Single Cycle Flip-Flop Error Localization
Try F3
Notes: Restoration ratios, do not address bugs are gone by the time you look at it

## Slide 30
30
A
B
X
Y
Z
F1
F2
F3
F4
F5
F6
F7
F8
1
1
0
1
0
1
1
0
1
1
0
Different
Error!
Cycle 2
0
Cycle 3
Cycle 4
Candidate FFs
Cycle 4: F6
Not a Potential Candidate
Cycle 3: F3
Single Cycle Flip-Flop Error Localization
Try F1
Two final candidates
Notes: Restoration ratios, do not address bugs are gone by the time you look at it

## Slide 31
31
Modified RTL design – Only during BMC
For each flip-flop:
D
1
0
S
Q
Insert MUX
Original
D Input
BMC-controlled
Select
BMC Flip-Flop Localization
Notes: Restoration ratios, do not address bugs are gone by the time you look at it

## Slide 32
BMC Flip-Flop Localization
32
Find candidates: satisfy signature consistency
X
Y
Z
F1
F2
F3
F4
F5
Module E
Input MISR
Output MISR
1 | 1 | 1 | 0 | 1 | 0
A
B
1 | 1 | 0 | 0 | 1 | 0
F6
F7
F8
Notes: Restoration ratios, do not address bugs are gone by the time you look at it

## Slide 33
33
Return all satisfying flip-flop candidates
Trace | Candidates
1 | Cycle 3 FF3, Cycle 4 FF6
2 | Cycle 1 FF4, Cycle 2 FF7
More aliased candidates
  Multiple traces satisfy signatures
BMC Flip-Flop Localization
BMC Tool
Notes: Restoration ratios, do not address bugs are gone by the time you look at it

## Slide 34
Aliased Traces
34
Trace 1
Output MISR
0 | 0 | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0 | 0
1 | 0 | 1 | 1 | 0 | 0
1 | 1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 1 | 0
X
Y
Z
X
Y
Z
1 | 1 | 0
0 | 1 | 0
1 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Trace 2
Output MISR
0 | 0 | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0 | 0
1 | 0 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 0
1 | 1 | 0 | 0 | 1 | 0
1 | 1 | 0
0 | 1 | 0
1 | 0 | 1
1 | 0 | 1
1 | 1 | 1
Trace 2 Injected Error
Trace 1 Injected Error
Final Signatures Match
1 | 1 | 0
1 | 1 | 0
0 | 1 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | 1
1 | 0 | 1
1 | 0 | 1
1 | 1 | 1
1 | 1 | 0
…
…
Notes: Restoration ratios, do not address bugs are gone by the time you look at it

## Slide 35
Signature Error Localization
35
Reduce or remove aliased candidates?
  Test traces in neighboring modules
Module A
Module D
Module
B
Module E
Module
C
Module F
Notes: Restoration ratios, do not address bugs are gone by the time you look at it

## Slide 36
Neighbor Consistency Checking
36
Test trace on Module D
  Compare vs. captured neighbor signature
Module
E
Module
D
Notes: Restoration ratios, do not address bugs are gone by the time you look at it

## Slide 37
37
Test Trace 1
1 | 0 | 0 | 0 | 1 | 0

1 | 0 | 0 | 0 | 1 | 0
Expected:
Trace | Candidates
1 | Cycle 3 FF3, Cycle 4 FF6
2 | Cycle 1 FF4, Cycle 2 FF7

Neighbor Consistency Checking
Module
E
Module
D
0
1
1
0
1
0
1
0
1
1
0
1
1
1
1
Notes: Restoration ratios, do not address bugs are gone by the time you look at it

## Slide 38
Trace | Candidates
1 | Cycle 3 FF3, Cycle 4 FF6
2 | Cycle 1 FF4, Cycle 2 FF7
38
Test Trace 2
0 | 1 | 0 | 0 | 1 | 1
1 | 0 | 0 | 0 | 1 | 0
Expected:
Neighbor Consistency Checking
Module
E
Module
D

0
1
1
0
1
0
1
0
1
1
0
1
0
1
1
Notes: Restoration ratios, do not address bugs are gone by the time you look at it

## Slide 39
Trace | Candidates
1 | Cycle 3 FF3, Cycle 4 FF6
2 | Cycle 1 FF4, Cycle 2 FF7
39
Only Trace 1 satisfies Module G
Rule out Trace 2
Candidates
Neighbor Consistency Checking
Module
E
Module
D

Notes: Restoration ratios, do not address bugs are gone by the time you look at it

## Slide 40
  1,000,000 random bit errors
    8 processor cores, crossbar interconnect
    8 L2 cache controllers, 4 memory controllers
E-QED Simulation Results
40
OpenSPARC T2
0.5 billion transistors
1 million flip-flops
    Commercial version: Sun UltraSPARC T2
Notes: Restoration ratios, do not address bugs are gone by the time you look at it

## Slide 41
41
100% Design Module Localization
E-QED (min, average, max) | 
Buggy design module | Uniquely identified: 100%

## Slide 42
42
50,000X Localization Factor
E-QED (min, average, max) | 
Buggy design module | Uniquely identified: 100%
Flip-flop Candidates (Out of ~1 million) | (5, 18, 26) flip-flops
  Localization Factor =
Total flip-flops in design
Number of flip-flop candidates

## Slide 43
43
E-QED (min, average, max) | 
Buggy design module | Uniquely identified: 100%
Flip-flop Candidates (Out of ~1 million) | (5, 18, 26) flip-flops
Area Overhead | 2.5% or less
  1.5% area overhead: ~70 flip-flop candidates
Low Area Overhead

## Slide 44
44
Overnight Localization
E-QED (min, average, max) | 
Buggy design module | Uniquely identified: 100%
Flip-flop Candidates (Out of ~1 million) | (5, 18, 26) flip-flops
Area Overhead | 2.5% or less
Debug Effort | Automatic
Runtime | (7, 8.7, 12) hours

## Slide 45
Related Work
Observability
e.g.,
trace buffers, assertions in hardware
Bayazit 05, Abramovici 06, Anis 07, Vali 16, …
Observability ≠ localization
Expensive or limited benefits

## Slide 46
Related Work
SAT for hardware debug
e.g.,
VLSI fault diagnosis, BackSpace derivatives
Sellers 68, Larrabee 92, De Paula 08, Zhu 11, …
Billion-transistor designs ?
Failure reproduction extremely difficult
Notes: Boolean techniques for hardware debug have their foundation in the 1960s… first work on using Boolean analysis for debug
Tab-backspace for failure reproduction

## Slide 47
Related Work
Data-driven debug
e.g.,
mining, bug positioning system
Li 10, De Orio 11,
Park 09, 10, …
False positives
Processor focus limited

## Slide 48
Related Work
Observability
e.g.,
trace buffers, assertions in hardware
Bayazit 05, Abramovici 06, Anis 07, Vali 16, …
E-QED:
low-cost,
effective
SAT for hardware debug
e.g.,
VLSI fault diagnosis, BackSpace derivatives
Sellers 68, Larrabee 92, De Paula 08, Zhu 11, …
E-QED:
scalable, fast,
no failure reproduction
Data-driven debug
e.g.,
mining, IFRA,
bug positioning system
Li 10, De Orio 11,
Park 09, 10, …
E-QED:
no false positives,
arbitrary designs
E-QED complementary
Notes: Nu-tab for rewrite rules
Backbones from princetion

## Slide 49: Symbolic QED for Logic Bugs
49
Pre-silicon formal verification
20 mins. to 7 hours
Automatic: no property / constraint writing
Billion-transistor chips
[Lin ITC 15, Singh IEEE TCAD 17]

## Slide 50
Acknowledgements

## Slide 51
51
E-QED
Automatic, overnight
  vs. manual, weeks / months per bug
Fine-grained localization
  From 1 million to 20 flip-flops
Scalable: billion-transistor design
Small area impact: 2.5% or less
  Many ways to reduce area impact
Notes: Scales
Automatic
Very large
First result of it’s kind

## Slide 52: Backups
52

## Slide 53
E-QED signature block
53
Reset 2
Reset 1
Design Module Boundary
D
Q
D
Q
D
Q
….
M
Interface Clock
D
Q
D
Q
D
Q
D
Q
D
Q
D
Q
Internal Logic
D
Q
D
Q
D
Q
….
C
….
K
….
K
Counter
MISR 1
MISR 2
Notes: Restoration ratios, do not address bugs are gone by the time you look at it

## Slide 54
Signature Generator
54
Need 2 MISRs: alternating reset
  Capture min N cycles, max 2N cycles
RST 1
RST 2
MISR 1
MISR 2
N
2N
3N
Notes: Restoration ratios, do not address bugs are gone by the time you look at it

## Slide 55: Full Results
55
 | Original tests (No QED) | New technique (after running QED versions of the original tests)
Number of Detected Errors | 2,832 | 12,555
Error Detection Latency (cycles) [Min, Avg, Max] | [793, 976K, 8.8M] | [19, 168, 763]
Number of flip-flop Candidates [Min, Avg, Max] | 9.3 * 105 (~all flip-flops in the design) | [5, 18, 36]
Number of Bug Traces [Min, Avg, Max] | N/A | [1, 1, 1]
Number of bits in a bug trace [Min., Avg, Max] | N/A | [109kb, 483kb, 1.74Mb]
BMC Runtime (minutes) [Min., Avg, Max] | N/A | [420, 526, 772]
Total signature analyzer area overhead | N/A | 2.5%
Clock speed impact | N/A | ~ 0%
Localization Factor [Min, Avg, Max] | 1x | [26,067x, 52,133x, 187,680x]

## Slide 56: Random Injection Statistics
56
Core | Number of Targeted FFs | 60,597
 | Number of Error Injections | 458,533
 | Number of Detected Errors | 3,872
 | Percentage of FFs with 1 Detected Error | 3.42%
L2C | Number of Targeted FFs | 18,369
 | Number of Error Injections | 138,997
 | Number of Detected Errors | 1,794
 | Percentage of FFs with 1 Detected Error | 5.53%
Crossbar | Number of Targeted FFs | 41,181
 | Number of Error Injections | 311,614
 | Number of Detected Errors | 3,576
 | Percentage of FFs with 1 Detected Error | 3.19%
MCU | Number of Targeted FFs | 12,007
 | Number of Error Injections | 90,856
 | Number of Detected Errors | 3,316
 | Percentage of FFs with 1 Detected Error | 12.78%

## Slide 57: Core Results
57
 |  | Signature Localization | Single FF Error Localization | NCC Localization
Processor Core | Number of Traces [Min, Avg, Max] | N/A | [1, 3, 8] | [1, 1, 1]
 | Number of FF Candidates [Min, Avg, Max] | 63,428 | [11, 54, 91] | [8, 16, 29]
 | Avg. Localization Factor | 14x | 16,805x | 58,133x
 | BMC Runtime (minutes) [Min, Avg, Max] | [62, 74, 77] | [303,416,478] | [49, 85, 114]

## Slide 58: Crossbar Results
58
 |  | Signature Localization | Single FF Error Localization | NCC Localization
Crossbar | Number of Traces [Min, Avg, Max] | N/A | [2, 12, 17] | [1, 1, 1]
 | Number of FF Candidates [Min, Avg, Max] | 41,521 | [31, 74, 130] | [5,23, 36]
 | Avg. Localization Factor | 21x | 12,263x | 40,440x
 | BMC Runtime (minutes) [Min, Avg, Max] | [53, 61, 72] | [379,421,450] | [54,142,205]

## Slide 59: L2 Cache Results
59
 |  | Signature Localization | Single FF Error Localization | NCC Localization
L2 Cache | Number of Traces [Min, Avg, Max] | N/A | [2, 14, 19] | [1, 1, 1]
 | Number of FF Candidates [Min, Avg, Max] | 31,675 | [28, 77, 154] | [7, 19, 33]
 | Avg. Localization Factor | 41x | 11,786x | 48,954x
 | BMC Runtime (minutes) [Min, Avg, Max] | [51, 58, 64] | [468,504,535] | [42,187,242]

## Slide 60: Memory Control Unit Results
60
 |  | Signature Localization | Single FF Error Localization | NCC Localization
Memory Control Unit | Number of Traces [Min, Avg, Max] | N/A | [3, 19, 24] | [1, 1, 1]
 | Number of FF Candidates [Min, Avg, Max] | 18,068 | [21, 67, 143] | [5, 11, 18]
 | Avg. Localization Factor | 72x | 13,544x | 84,557x
 | BMC Runtime (minutes) [Min, Avg, Max] | [35, 37, 41] | [315,387,428] | [78,163,251]

## Slide 61: Area Overhead
61
Maximum number of unique candidate traces observed
Before and after Neighbor Consistency Checking (NCC)
For different area overheads
  Varying the number of MISR bits per signal traced

## Slide 62: MISR Insertion Optimization
62
Maximum number of unique candidate traces observed after NCC
with and without additional MISRs
  L2 cache banks, processor instruction fetch
For different MISR sizes (bits per signal traced)

## Slide 63: Errors masked by Initial States
63
Percentage of errors masked
By symbolic initialization of internal FFs
Formal analysis of 1,000 cycles prior to error detection

## Slide 64: Runtime Comparison
64
Signature Cycles | Crossbar Arbiter (1,000 FFs) | L2C SubModule (5,000 FFs) | Memory Control Unit (20,000 FFs) | Processor (60,000 FFs)
5,000 | 47 | 351 | 1058 | 2623
10,000 | 139 | 993 | 2391 | 48 hr. Timeout
25,000 | 457 | 2103 | 48 hr. Timeout | 48 hr. Timeout
50,000 | 1472 | 48 hr. Timeout | 48 hr. Timeout | 48 hr. Timeout
100,000 | 48 hr. Timeout | 48 hr. Timeout | 48 hr. Timeout | 48 hr. Timeout
Runtime results for different sized Modules
Analyzed over 5,000 to 100,000 cycles

## Slide 65: Oracle Injection Statistics
65
Core | Number of Targeted FFs | 60,597
 | Number of Error Injections | 500,000
 | Number of Detected Errors | 76,902
 | Percentage of FFs with at least 1 Detected Error | 21.67%
L2C | Number of Targeted FFs | 18,369
 | Number of Error Injections | 800,000
 | Number of Detected Errors | 157,211
 | Percentage of FFs with at least 1 Detected Error | 29.64%
Crossbar | Number of Targeted FFs | 41,181
 | Number of Error Injections | 800,000
 | Number of Detected Errors | 98,058
 | Percentage of FFs with at least 1 Detected Error | 18.02%
MCU | Number of Targeted FFs | 12,007
 | Number of Error Injections | 800,000
 | Number of Detected Errors | 184,853
 | Percentage of FFs with at least 1 Detected Error | 32.79%

## Slide 66: Oracle Injection Results
66
 |  | Signature Localization | Single FF Error Localization | NCC Localization
Processor Core | Number of Traces | N/A | [1, 3, 8] | [1, 1, 1]
 | Number of Candidates | 63,428 | [7, 50, 101] | [7, 15, 31]
 | Avg. Localization Factor | 14x | 18,768x | 62,560x
 | BMC Runtime (minutes) | [62, 74, 77] | [287,423,486] | [49, 85, 114]
L2 Cache | Number of Traces | N/A | [2, 13, 21] | [1, 1, 1]
 | Number of Candidates | 31,675 | [25, 79, 159] | [7, 20, 35]
 | Avg. Localization Factor | 41x | 11,879x | 46,920x
 | BMC Runtime (minutes) | [46, 58, 67] | [442,501,548] | [42,187,242]
Crossbar | Number of Traces | N/A | [1, 12, 17] | [1, 1, 1]
 | Number of Candidates | 41,521 | [31, 74, 130] | [5,21, 38]
 | Avg. Localization Factor | 21x | 12,681x | 44,686x
 | BMC Runtime (minutes) | [51, 61, 79] | [357,416,467] | [54,142,205]
Memory Control Unit | Number of Traces | N/A | [2, 18, 25] | [1, 1, 1]
 | Number of Candidates | 18,068 | [21, 67, 143] | [5, 11, 18]
 | Avg. Localization Factor | 72x | 14,006x | 85,309x
 | BMC Runtime (minutes) | [32, 34, 47] | [315,387,428] | [78,163,251]

## Slide 67
BMC Bit Error Localization
67
Model
  Design RTL
    Modified to inject 1 bit error in 1 cycle
Property
  After N cycles (from counter)
  Inputs = Input Signature && Outputs = Output Signature
Notes: Restoration ratios, do not address bugs are gone by the time you look at it

## Slide 68
Modified design – enable single bit error
BMC Bit Error Localization
68
For each FF:
D
1
0
S
Q
Insert MUX
Original
D Input
FF N
Error Bit
Select for FF N
Notes: Restoration ratios, do not address bugs are gone by the time you look at it

## Slide 69
Modified design: Model for BMC
BMC Bit Error Localization
69
Error
Selects
Module with MUXes
for all K FFs
K
Reset
Bit Error Control
Bit error control
BMC control signals
Output
Signature
Input
Signature
Only for BMC: Fabricated design unchanged
Notes: Restoration ratios, do not address bugs are gone by the time you look at it

## Slide 70
Bit-flip Localization
70
LFSR Signature  localization constraint
Module D
with MUXes
for all K FFs
Reset
Bit Error Control
Bit error control
Module Output Signature
Module Input Signature
Test BMC property
  Inputs = Input Signature && Outputs = Output Signature
  Find bit-flip candidates
Notes: Restoration ratios, do not address bugs are gone by the time you look at it

## Slide 71
BMC Result
  Multiple runs: Candidate list of FFs
BMC Bit Error Localization
71
Cycle 84: FF 383
Cycle 96: FF 2380
Cycle 96: FF 2383
Cycle 121: FF 1107
Cycle 148: FF 654
Cycle 149: FF 682
At the given cycle:
FF bit error causes traced (incorrect) output
FF #  Bit error Control Value
Notes: Restoration ratios, do not address bugs are gone by the time you look at it

## Slide 72: QED Transforms
72
Uncore, accelerators
Processor cores
EDDI-V
CFTSS-V
CFCSS-V
PLC
Fast QED
Hybrid QED

## Slide 73: QED Example: Duplicate & Check
73
void matgen (REAL a[], int lda, int n, REAL b[], REAL *norma)
{
int init, i, j;
init = 1325;
*norma = 0.0;
for (j = 0; j < n; j++) {
for (i = 0; i < n; i++) {
init = 3125*init % 0x100000000l;
a[lda*j+i] = (init - 32768.0)/16384.0;
*norma = (a[lda*j+i] > *norma) ? a[lda*j+i] : *norma;
}
}
for (i = 0; i < n; i++) {
b[i] = 0.0;
}
for (j = 0; j < n; j++) {
for (i = 0; i < n; i++) {
b[i] = b[i] + a[lda*j+i];
}
}
return;
}
void dgefa(REAL a[], int lda, int n, int ipvt[], int *info){
/* internal variables */
REAL t;
int j,k,kp1,l,nm1;
/* gaussian elimination with partial pivoting */
*info = 0;
nm1 = n - 1;
if (nm1 >= 0) {
for (k = 0; k < nm1; k++) {
kp1 = k + 1;
/* find l = pivot index */
l = idamax(n-k,&a[lda*k+k],1) + k;
ipvt[k] = l;
/* zero pivot implies this column already
triangularized */
if (a[lda*k+l] != ZERO) {
/* interchange if necessary */
if (l != k) {
t = a[lda*k+l];
a[lda*k+l] = a[lda*k+k];
a[lda*k+k] = t;
}
/* compute multipliers */
t = -ONE/a[lda*k+k];
dscal(n-(k+1),t,&a[lda*k+k+1],1);
/* row elimination with column indexing */
for (j = kp1; j < n; j++) {
t = a[lda*j+l];
if (l != k) {
a[lda*j+l] = a[lda*j+k];
a[lda*j+k] = t;
}
daxpy(n-(k+1),t,&a[lda*k+k+1],1,
&a[lda*j+k+1],1);
}
}
else {
*info = k;
}
}
}
ipvt[n-1] = n-1;
if (a[lda*(n-1)+(n-1)] == ZERO) *info = n-1;
checkExpected(a, ipvt, info);
return;
}
void dgesl(REAL a[],int lda,int n,int ipvt[],REAL b[],int job )
{
REAL t;
int k,kb,l,nm1;
nm1 = n - 1;
if (job == 0) {
/* job = 0 , solve a * x = b
first solve l*y = b */
if (nm1 >= 1) {
for (k = 0; k < nm1; k++) {
l = ipvt[k];
t = b[l];
if (l != k){
b[l] = b[k];
b[k] = t;
}
daxpy(n-(k+1),t,&a[lda*k+k+1],1,&b[k+1],1 );
}
}
/* now solve u*x = y */
for (kb = 0; kb < n; kb++) {
k = n - (kb + 1);
b[k] = b[k]/a[lda*k+k];
t = -b[k];
daxpy(k,t,&a[lda*k+0],1,&b[0],1 );
}
}
else {
Trace
Validation program
Check end_result
R1 ← R1 + 5
R2 ← R2 – R1
R3 ← R1 * R2
Very
Long!
Notes: 73

## Slide 74: QED Example: Duplicate & Check
74
void matgen (REAL a[], int lda, int n, REAL b[], REAL *norma)
{
int init, i, j;
init = 1325;
*norma = 0.0;
for (j = 0; j < n; j++) {
for (i = 0; i < n; i++) {
init = 3125*init % 0x100000000l;
a[lda*j+i] = (init - 32768.0)/16384.0;
*norma = (a[lda*j+i] > *norma) ? a[lda*j+i] : *norma;
}
}
for (i = 0; i < n; i++) {
b[i] = 0.0;
}
for (j = 0; j < n; j++) {
for (i = 0; i < n; i++) {
b[i] = b[i] + a[lda*j+i];
}
}
return;
}
void dgefa(REAL a[], int lda, int n, int ipvt[], int *info){
/* internal variables */
REAL t;
int j,k,kp1,l,nm1;
/* gaussian elimination with partial pivoting */
*info = 0;
nm1 = n - 1;
if (nm1 >= 0) {
for (k = 0; k < nm1; k++) {
kp1 = k + 1;
/* find l = pivot index */
l = idamax(n-k,&a[lda*k+k],1) + k;
ipvt[k] = l;
/* zero pivot implies this column already
triangularized */
if (a[lda*k+l] != ZERO) {
/* interchange if necessary */
if (l != k) {
t = a[lda*k+l];
a[lda*k+l] = a[lda*k+k];
a[lda*k+k] = t;
}
/* compute multipliers */
t = -ONE/a[lda*k+k];
dscal(n-(k+1),t,&a[lda*k+k+1],1);
/* row elimination with column indexing */
for (j = kp1; j < n; j++) {
t = a[lda*j+l];
if (l != k) {
a[lda*j+l] = a[lda*j+k];
a[lda*j+k] = t;
}
daxpy(n-(k+1),t,&a[lda*k+k+1],1,
&a[lda*j+k+1],1);
}
}
else {
*info = k;
}
}
}
ipvt[n-1] = n-1;
if (a[lda*(n-1)+(n-1)] == ZERO) *info = n-1;
checkExpected(a, ipvt, info);
return;
}
void dgesl(REAL a[],int lda,int n,int ipvt[],REAL b[],int job )
{
REAL t;
int k,kb,l,nm1;
nm1 = n - 1;
if (job == 0) {
/* job = 0 , solve a * x = b
first solve l*y = b */
if (nm1 >= 1) {
for (k = 0; k < nm1; k++) {
l = ipvt[k];
t = b[l];
if (l != k){
b[l] = b[k];
b[k] = t;
}
daxpy(n-(k+1),t,&a[lda*k+k+1],1,&b[k+1],1 );
}
}
/* now solve u*x = y */
for (kb = 0; kb < n; kb++) {
k = n - (kb + 1);
b[k] = b[k]/a[lda*k+k];
t = -b[k];
daxpy(k,t,&a[lda*k+0],1,&b[0],1 );
}
}
else {
QED Trace
Validation program
Check end_result
R16 ← R16 + 5
R18 ← R18 – R16
R19 ← R16 * R18
R1 ← R1 + 5
R2 ← R2 – R1
R3 ← R1 * R2
R1 == R16
R2 == R18
R3 == R19
R16 ← R1; R18 ← R2; R19 ← R3
Quick!
Notes: 74

## Slide 75: Diversity-Enhanced QED
75
void matgen (REAL a[], int lda, int n, REAL b[], REAL *norma)
{
int init, i, j;
init = 1325;
*norma = 0.0;
for (j = 0; j < n; j++) {
for (i = 0; i < n; i++) {
init = 3125*init % 0x100000000l;
a[lda*j+i] = (init - 32768.0)/16384.0;
*norma = (a[lda*j+i] > *norma) ? a[lda*j+i] : *norma;
}
}
for (i = 0; i < n; i++) {
b[i] = 0.0;
}
for (j = 0; j < n; j++) {
for (i = 0; i < n; i++) {
b[i] = b[i] + a[lda*j+i];
}
}
return;
}
void dgefa(REAL a[], int lda, int n, int ipvt[], int *info){
/* internal variables */
REAL t;
int j,k,kp1,l,nm1;
/* gaussian elimination with partial pivoting */
*info = 0;
nm1 = n - 1;
if (nm1 >= 0) {
for (k = 0; k < nm1; k++) {
kp1 = k + 1;
/* find l = pivot index */
l = idamax(n-k,&a[lda*k+k],1) + k;
ipvt[k] = l;
/* zero pivot implies this column already
triangularized */
if (a[lda*k+l] != ZERO) {
/* interchange if necessary */
if (l != k) {
t = a[lda*k+l];
a[lda*k+l] = a[lda*k+k];
a[lda*k+k] = t;
}
/* compute multipliers */
t = -ONE/a[lda*k+k];
dscal(n-(k+1),t,&a[lda*k+k+1],1);
/* row elimination with column indexing */
for (j = kp1; j < n; j++) {
t = a[lda*j+l];
if (l != k) {
a[lda*j+l] = a[lda*j+k];
a[lda*j+k] = t;
}
daxpy(n-(k+1),t,&a[lda*k+k+1],1,
&a[lda*j+k+1],1);
}
}
else {
*info = k;
}
}
}
ipvt[n-1] = n-1;
if (a[lda*(n-1)+(n-1)] == ZERO) *info = n-1;
checkExpected(a, ipvt, info);
return;
}
void dgesl(REAL a[],int lda,int n,int ipvt[],REAL b[],int job )
{
REAL t;
int k,kb,l,nm1;
nm1 = n - 1;
if (job == 0) {
/* job = 0 , solve a * x = b
first solve l*y = b */
if (nm1 >= 1) {
for (k = 0; k < nm1; k++) {
l = ipvt[k];
t = b[l];
if (l != k){
b[l] = b[k];
b[k] = t;
}
daxpy(n-(k+1),t,&a[lda*k+k+1],1,&b[k+1],1 );
}
}
/* now solve u*x = y */
for (kb = 0; kb < n; kb++) {
k = n - (kb + 1);
b[k] = b[k]/a[lda*k+k];
t = -b[k];
daxpy(k,t,&a[lda*k+0],1,&b[0],1 );
}
}
else {
QED Trace
Validation program
Many diversity techniques
e.g., ED4I [Oh IEEE Trans. Comp. 02]
14 10
6 2
R1 ← a + b
R1
R18 ← 5a' + 5b'
R18
a ← 1; a' ← a; b ← 1, b' ← b
5×R1 == R18
Notes: 75

## Slide 76
Signature Generator
76
To provide initial signature value for BMC
  Must reset signature generator periodically
Is one signature enough? NO
Example: 1000 cycle signature window
  500 cycle bug detection latency
  50% probability of capturing the bug

## Slide 77
Case Study on Speed Failure Causes in a Microprocessor , IEEE D&T 2008
Kip Killpack, Suriyaprakash Natarajan, and Arun Krishnamachary Intel
Pouria Bastani UCSB
New challenges in delay testing of nanometer, multigigahertz designs, IEEE D&T 2004
T.M. Mak Intel
A. Krstic Cadence
K.-T. Cheng, Li.-C. Wang UCSB